#### TABLE OF CONTENTS

I. 	General description	3

II	Capacitance ranges	3

III 	Dimensions	4

IV 	Dielectric characteristics	10

V 	How to order	11

VI 	Packaging	12

# I. General description

These discs capacitors have been developed for use in all electronic applications with voltage rating from 1KV to 15KV. Suitable for LAN/WLAN interfaces, DC-DC converters, modems and communication etc… Some of the main advantages of these capacitors are the high reliability and low loss at wide frequency range.

This family is RoHS compliant.

# II Capacitance ranges

| Dielectric Type | Rated Voltage | Capacitance Range |
| --- | --- | --- |
|  |  | 1R5 | 2R0 | 3R0 | 4R0 | 5R0 | 6R0 | 7R0 | 8R0 | 9R0 | 100 | 120 | 150 | 180 | 220 | 270 | 330 | 390 | 470 | 560 | 680 | 820 | 101 | 121 | 151 | 181 | 221 | 271 | 331 | 391 | 471 | 561 | 681 | 821 | 102 |
| NP0 | 3KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 6KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 10KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 15KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 20KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| SL | 1KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 6KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 10KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 15KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 20KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

| Dielectric Type | Rated Voltage | Capacitance Range |
| --- | --- | --- |
|  |  | 101 | 121 | 151 | 181 | 221 | 271 | 331 | 391 | 471 | 561 | 681 | 821 | 102 | 122 | 152 | 182 | 222 | 272 | 332 | 392 | 472 | 562 | 682 | 822 | 103 | 153 | 183 | 223 | 273 | 333 | 393 | 473 |
| X7R | 1KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Y5P | 1KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 10KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 12KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 15KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Y5S | 3KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 6KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 10KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 12KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 15KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Y5U | 1KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 10KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 12KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 15KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Y5V | 1KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 2KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 3KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 10KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 12KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 15KV |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

# III Dimensions

| NP0 |
| --- |
| Rated Voltage (KV) | Capacitance Value (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 3 | 2 | 7.5 ± 1.5 | 5.5 | 6.0 |
|  | 5 to 33 |  | 7.5 |  |
|  | 39 to 47 |  | 8.0 |  |
|  | 56 |  | 8.5 |  |
|  | 68 |  | 9.0 |  |
|  | 82 |  | 10.0 |  |
|  | 100 |  | 11.0 |  |
| 6 | 2 | 7.5 ± 1.5 | 7.0 | 6.0 |

| SL |
| --- |
| Rated Voltage (KV) | Capacitance Value (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 1 | 10 to 47 | 5.0 ± 1.0 | 5.5 | 3.0 |
|  | 56 |  | 6.0 |  |
|  | 68 |  | 6.5 |  |
|  | 82 |  | 7.0 |  |
|  | 100 |  | 7.5 |  |
|  | 120 |  | 8.0 |  |
|  | 150 |  | 8.5 |  |
|  | 180 |  | 9.0 |  |
|  | 220 |  | 10.0 |  |
|  | 270 |  | 11.0 |  |
|  | 330 |  | 11.5 |  |
|  | 390 |  | 12.5 |  |
|  | 470 |  | 13.5 |  |
|  | 560 |  | 14.5 |  |
|  | 680 |  | 15.0 |  |
|  | 820 |  | 15.5 |  |
|  | 1000 |  | 16.0 |  |
| 2 | 10 to 47 | 5.0 ± 1.0 | 5.5 | 5.0 |
|  | 56 |  | 6.0 |  |
|  | 68 |  | 6.5 |  |
|  | 82 |  | 7.0 |  |
|  | 100 |  | 7.5 |  |
|  | 120 |  | 8.0 |  |
|  | 150 |  | 8.5 |  |
|  | 180 |  | 9.0 |  |
|  | 220 |  | 10.0 |  |
|  | 270 |  | 11.0 |  |
|  | 330 | 7.5 ± 1.0 | 11.5 |  |
|  | 390 |  | 12.5 |  |
|  | 470 |  | 13.5 |  |
|  | 560 |  | 14.5 |  |
|  | 680 |  | 16.0 |  |

| SL |
| --- |
| Rated Voltage (KV) | Capacitance Value (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 3 | 3 to 33 | 7.5 ± 1.5 | 7.0 | 6.0 |
|  | 39 to 47 |  | 7.5 |  |
|  | 56 |  | 8.0 |  |
|  | 68 |  | 8.5 |  |
|  | 82 |  | 9.5 |  |
|  | 100 to 150 |  | 10.5 |  |
|  | 180 |  | 11.0 |  |
|  | 220 |  | 12.0 |  |
|  | 270 |  | 13.0 |  |
|  | 330 |  | 14.0 |  |
|  | 390 |  | 15.0 |  |
|  | 470 |  | 16.0 |  |
| 6 | 3 to 33 | 7.5 ± 1.5 | 7.5 | 6.0 |
|  | 39 |  | 8.0 |  |
|  | 47 |  | 8.5 |  |
|  | 56 |  | 9.0 |  |
|  | 68 |  | 9.5 |  |
|  | 82 |  | 10.5 |  |
|  | 100 |  | 11.5 |  |
|  | 120 |  | 12 |  |

| X7R |
| --- |
| Rated Voltage (KV) | CapacitanceValue (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 1 | 100 to 560 | 5.0 ± 1.0 | 6.0 | 3.0 |
|  | 680 |  | 6.5 |  |
|  | 820 to 1000 |  | 7.0 |  |
|  | 1200 |  | 7.5 |  |
|  | 1500 |  | 8.0 |  |
|  | 1800 |  | 8.5 |  |
|  | 2200 |  | 9.0 |  |
|  | 2700 |  | 9.5 |  |
|  | 3300 |  | 10.0 |  |
|  | 3900 |  | 11.0 |  |
|  | 4700 |  | 11.5 |  |
|  | 5600 |  | 12.0 |  |
|  | 6800 |  | 13.5 |  |
|  | 8200 |  | 14.5 |  |
|  | 10000 |  | 15.5 |  |
|  | 22000 |  | 16.5 |  |

| X7R |
| --- |
| Rated Voltage (KV) | CapacitanceValue (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 2 | 100 to 150 | 5.0 ± 1.0 | 6.0 | 5.0 |
|  | 180 |  | 6.5 |  |
|  | 220 to 270 |  | 7.0 |  |
|  | 330 |  | 7.5 |  |
|  | 390 |  | 8.0 |  |
|  | 470 |  | 8.5 |  |
|  | 560 |  | 9.0 |  |
|  | 680 |  | 9.5 |  |
|  | 820 |  | 10.0 |  |
|  | 1000 |  | 11.0 |  |
|  | 1200 | 7.5 ± 1.5 | 11.5 |  |
|  | 1500 |  | 12.0 |  |
|  | 1800 |  | 13.5 |  |
|  | 2200 |  | 14.5 |  |
|  | 2700 |  | 15.5 |  |
|  | 3300 |  | 17.0 |  |
|  | 3900 |  | 18.0 |  |
|  | 4700 |  | 19.5 |  |
| 3 | 100 | 7.5 ± 1.5 | 6.0 | 6.0 |
|  | 120 |  | 6.5 |  |
|  | 150 to 180 |  | 7.0 |  |
|  | 220 |  | 7.5 |  |
|  | 270 |  | 8.0 |  |
|  | 330 |  | 8.5 |  |
|  | 390 |  | 9.0 |  |
|  | 470 |  | 9.5 |  |
|  | 560 |  | 10.0 |  |
|  | 680 |  | 10.5 |  |
|  | 820 |  | 11.5 |  |
|  | 1000 |  | 12.0 |  |
|  | 1200 |  | 13.0 |  |
|  | 1500 |  | 14.5 |  |
|  | 1800 | 10.0 ± 2.0 | 15.5 |  |
|  | 2200 |  | 16.5 |  |
|  | 2700 |  | 18.0 |  |

| Y5P |
| --- |
| Rated Voltage (KV) | CapacitanceValue (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 1 | 100 to 270 | 5.0 ± 1.0 | 7.5 | 3.0 |
|  | 330 to 390 |  | 8.0 |  |
|  | 470 |  | 8.5 |  |
|  | 560 |  | 9.0 |  |
|  | 680 to 820 |  | 10.0 |  |
|  | 1000 |  | 11.0 |  |
|  | 1200 |  | 11.5 |  |
|  | 1500 |  | 12.0 |  |
|  | 1800 |  | 13.5 |  |
|  | 2200 |  | 14.5 |  |
|  | 2700 |  | 15.0 |  |
|  | 3300 |  | 15.5 |  |
|  | 3900 |  | 16.5 |  |
|  | 4700 |  | 17.0 |  |
|  | 5600 |  | 17.5 |  |
|  | 6800 |  | 18.0 |  |
|  | 8200 |  | 18.5 |  |
|  | 10000 |  | 19.0 |  |
| 2 | 100 to 270 | 5.0 ± 1.0 | 7.5 | 5.0 |
|  | 330 to 390 |  | 8.0 |  |
|  | 470 |  | 8.5 |  |
|  | 560 |  | 9.0 |  |
|  | 680 to 820 |  | 10.0 |  |
|  | 1000 |  | 11.0 |  |
|  | 1200 |  | 11.5 |  |
|  | 1500 | 7.5 ± 1.5 | 12.0 |  |
|  | 1800 |  | 13.5 |  |
|  | 2200 |  | 14.5 |  |
|  | 2700 |  | 15.0 |  |
|  | 3300 |  | 15.5 |  |
|  | 3900 |  | 16.5 |  |
|  | 4700 |  | 17.0 |  |
| 3 | 100 to 220 | 7.5 ± 1.5 | 7.5 | 6.0 |
|  | 270 to 330 |  | 8.0 |  |
|  | 390 |  | 9.0 |  |
|  | 470 |  | 10.0 |  |
|  | 560 |  | 10.5 |  |
|  | 680 |  | 11.0 |  |
|  | 820 |  | 12.0 |  |
|  | 1000 |  | 12.5 |  |
|  | 1200 |  | 13.5 |  |
|  | 1500 |  | 14.5 |  |
|  | 1800 | 10.0 ± 2.0 | 15.5 |  |
|  | 2200 |  | 16.5 |  |
|  | 2700 to 3300 |  | 18.0 |  |

| Y5S |
| --- |
| Rated Voltage (KV) | CapacitanceValue (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 3 | 100 | 7.5 ± 1.5 | 5.5 | 5.0 |
|  | 150 |  | 6.5 |  |
|  | 220 |  | 7.5 |  |
|  | 330 |  | 8.5 |  |
|  | 390 |  | 9.0 |  |
|  | 470 |  | 9.5 |  |

| Y5U |
| --- |
| Rated Voltage (KV) | CapacitanceValue (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 1 | 470 to 680 | 5.0 ± 1.0 | 5.5 | 3.0 |
|  | 1000 |  | 6.0 |  |
|  | 1500 |  | 7.0 |  |
|  | 2200 |  | 8.0 |  |
|  | 3300 |  | 9.0 |  |
|  | 4700 |  | 10.5 |  |
|  | 6800 |  | 12.5 |  |
|  | 10000 |  | 14.5 |  |
| 2 | 470 to 680 | 5.0 ± 1.0 | 5.5 | 5.0 |
|  | 1000 |  | 6.0 |  |
|  | 1500 |  | 7.0 |  |
|  | 2200 |  | 8.0 |  |
|  | 3300 |  | 9.0 |  |
|  | 4700 |  | 10.5 |  |
|  | 6800 | 7.5 ± 1.5 | 12.5 |  |
|  | 10000 |  | 14.5 |  |
| 3 | 470 | 7.5 ± 1.5 | 6.0 | 6.0 |
|  | 680 |  | 6.5 |  |
|  | 1000 |  | 7.5 |  |
|  | 1500 |  | 8.5 |  |
|  | 2200 |  | 9.5 |  |
|  | 3300 |  | 11.5 |  |
|  | 4700 |  | 12.5 |  |
|  | 6800 | 10.0 ± 2.0 | 15.0 |  |

| Y5V |
| --- |
| Rated Voltage (KV) | CapacitanceValue (pF) | Lead Spacing (mm) | Body Diameter (mm) | Body Thickness (mm) |
| 3 | 1000 to 2200 | 5.0 ± 1.0 | 8.0 | 6.0 |

For other products, please, contact us.

# IV Dielectric characteristics

| Dielectric code | Dielectric Type | EIA Class | Temperature Range | Temperature coefficient | Max C/C vs Temperature |
| --- | --- | --- | --- | --- | --- |
| N | NP0 | Class I | -55°C / +125°C | 0 ± 30ppm / °C | NA |
| D | SL | Class I | -25°C / +85°C | +350~1000ppm / °C | NA |
| X | X7R | Class II | -55°C / +125°C | NA | ± 15% max |
| P | Y5P | Class II | -25°C / +85°C | NA | ± 10% max |
| V | Y5S | Class II | -25°C / +85°C | NA | ± 22% max |
| E | Y5U | Class II | -25°C / +85°C | NA | +22% / -56% |
| Y | Y5V | Class II | -25°C / +85°C | NA | +22% / -82% |

| Dielectric code | Dielectric Type | Aging 1 | Insulation Resistance 2 | Q factor 3 | Dissipation factor | Voltage Proof 4 |
| --- | --- | --- | --- | --- | --- | --- |
| N | NP0 | None | 10G( or 500(F | ≤30pF Q≥1000 >30pF Q≥400+20*C | - | ≤ 2KV 200% Ur 3KV 175% Ur ≥6KV 150% Ur |
| D | SL | 1.5% | 10G( or 500(F | ≤30pF Q≥1000 >30pF Q≥400+20*C | - |  |
| X | X7R | 3.5% | 10G( or 500(F | - | ≤ 2.5% |  |
| P | Y5P | 3.5% | 10G( or 500(F | - | ≤ 2.5% |  |
| V | Y5S | 3.5% | 10G( or 500(F | - | ≤ 1% |  |
| E | Y5U | 5.0% | 10G( or 500(F | - | ≤ 5.0% |  |
| Y | Y5V | 7.5% | 10G( or 500(F | - | ≤ 5.0% |  |

(1): per decade hour (typical)

(2): whichever is the smaller (500V applied)

(3): “C” is the capacitance value in pF

(4): “Ur” is the rated voltage in volt

For Q factor and Dissipation factor, the frequency is 1MHz for N and D dielectrics, 1KHz for the other dielectrics.

# V How to order

# VI Packaging

PACKAGING QUANTITY:

Bulk: 		500 or 1000 pieces per pack, other according to request.

Reel:		1500 or 2000 pieces per reel

Ammo Box:	1000 or 1500 pieces per box

Tape dimensions (for Reel and Ammo pack)

Reel dimensions

Ammo dimensions

# Text boxes

Lead Spacing

5 = 5.00 mm

6 = 6.35 mm

7 = 7.50 mm

A = 10.0 mm

B = 12.5 mm

T

LS

Lead length

4.0 mm

max

D type

D

5

Lead Diameter

1: Ø = 0.50 mm

2: Ø = 0.60 mm

3: Ø = 0.65 mm

4: Ø = 0.80 mm

D

Tolerance

Class I < 10pF

C ((0.25%)

D ((0.50%)

Class I ≥10pF

H ((3%)

J ((5%)

Class II

K ((10%)

M ((20%)

Capacitance

1st two digits are significant; third digit denotes number of zeros

Exemples:

101=100pF

472= 4.7nF

683 = 68nF

104 = 0.1µF

103M

2KV

Packaging

Bulk (lead length)

H = 3.1 mm

C = 3.5mm

S = 5.0mm

M = 10.0mm

L = 25.0mm mini

Reel

T

Ammo Box

A

Dielectric

N = NP0

D = SL

X = X7R

P = Y5P

V = Y5S

E = Y5U

Y = Y5V

Rated

Voltage

1st two digits are significant; third digit denotes number of zeros

Exemples:

102=1000V

202=2000V

602=6000V

103=10000V

153=15000V

203=20000V

T

1

K

471

103M

2KV

X

Capacitor

Shape

Type

S

D

S type

d

Lead length

d

L

102

S

4.0 mm

max

LS